# Choosing components for a triac's snubber

I'm interfacing the BT139-600 TRIAC with this MOC3051-M Opto-triac. I want to build a snubber circuit for the TRIAC as shown in the MOC3051M opto-triac's datasheet @ page 8, figure 12.

The load will be a 230V AC, 4A motor. What are the recommended characteristics of the Rs, Cs and MOV in that schematic (the type of the resistor and capacitor, power specifications, voltage limits)? Would this components be a good pick for the snubber?
Cs: Ceramic Capacitor 10nF
Rs: 33 Ohm 5W wirewound resistor
MOV: JVR14N431K 275V AC MOV Varistor
Do I also need a snubber for the triac driver?

Answer:
Please specify load characteristics and use of circuit. Ideally a circuit diagram. The snubber's role is to dissipate transient energy which is looking for a home at switch off time. We need to know how much energy is there and how it is "stored" to know what sort of home it needs. As a guide you want an energy sink that will stop reactive voltage rising dangerously high, that will dissipate available ractive energy prior to the next switching cycle and which has minimal possible effect the rest of the time. Not magic, just compromise. – Russell McMahon Aug 3 '11 at 2:09
- I've updated my question, so that it would be more clear. – m.Alin Aug 21 '11 at 12:02
- Wouldn't a 10nF capacitor quickly be charged up to the MOV clamping voltage, by the inductance in the electric motor? 10nF at 430V is 924 millijoule. For this cap to hold the energy of the motor inductance, said inductance must be less than ~ 100uH. Is it? – avl_sweden Jul 21 '15 at 20:43
- 1
  @avl_sweden, the triac won't switch off until the motor current has fallen to near-zero. Then the concern becomes dV/dT as the voltage across the triac jumps to the line voltage. – Technophile Oct 24 '15 at 15:56